Spark Terasort and CRAIL
www.crail.io

---
I/O Hardware Trends
Speed
Diversity
- Network interconnects have evolved from
  - Gbps bandwidth to 100Gbps
  - 100us delay to 1us delay
- Storage technology has evolved
  - Factor 100x-1000x

---
I/O API Trends
Traditional
Modern
       Storage Network
       Storage Network
    Runtime
    Runtime
    Runtime
    Runtime
Application
Application
Application
Application
SPDK
RDMA/DPDK
OS Kernel
File System
LVM
Sockets
Multipath Driver
TCP/IP
Block Layer
No moving components
Latency in microseconds (usecs)
1-10+ GB/sec bandwidth
Dense packing and energy efficient
Ethernet
SCSI Layer
FC
iSCSI
SAS
NVMeOF
PCIe NVMe
Spinning Disk
1Gbs Ethernet
100Gbps Ethernet
Modern APIs for Networking and Storage offer asynchronous
non-blocking user-level access to hardware
OS kernel
OS kernel
OS kernel
OS kernel

---
Let's Use it!
SQL
Streaming
MLlib
GraphX
Spark
High-Performance RDMA network
DRAM
Flash
Many use cases:
- Improve performance
- Storage disaggregation
- Mix different storage technologies

---
Case Study: Sorting in Spark
Cores
Map
Reduce
Input
Output
Sort
Net
Ser
Sort
Net
Ser
Sort
Net
Ser
No moving components
Latency in microseconds (usecs)
1-10+ GB/sec bandwidth
Dense packing and energy efficient
store
read & classify
shuffle
- Map task classify data into local files (typically absorbed by buffer cache)
- Reduce task fetch remote files over the network
- Sorting requires the entire data set to be shuffled over the network

---
How is the Network Used?
No moving components
Latency in microseconds (usecs)
1-10+ GB/sec bandwidth
Dense packing and energy efficient
Only 5-10 Gpbs of the network is being used

---
What is the Problem
TeraSort
application
Spark Core
sockets
FileSystem
Serializer
IP/TCP
Block Layer
HDFS
Ethernet
SCSI Layer
JVM
NIC
NIC
- Application use the legacy APIs
- Applications themselves are heavily layered!
- Overhead during local file system writing
- Overhead during network processing
  - Data copies, context switches, cache pollution, etc
OS kernel

---
Example: Shuffle Writer (map)
Object
Buffer
External Sorter
Buffer
Kryo
Buffer
BufferedOutputStream
Buffer
JNI backend
Buffer
File System Buffer Cache

---
Example: Shuffle Reader (reduce)
getBlockInfo
Spark
Driver
getBlockData
Object
Buffer
Kryo
NettyServer/
BlockManager
Buffer
Buffer
NettyClient
Buffer
Cache
Buffer
Buffer
Buffer
Socket
network

---
Other Challenges
Node 1
Spark
Disaggregated
memory
Node 2
Spark
Disaggregated
Flash
Node 3
Spark
Network
Storage
Compute
- Can't easily exploit new I/O properties, e.g., local ~= remote
  - Difficult to disaggregate memory and storage
  - Difficult to leverage storage hierarchies

---
The Crail Project:
Performance View
Fast distributed storage for temporary data
data is exchanged directly between Spark and I/O devices (network & storage)
Map Reduce, Page Rank ..
Application
Spark, Flink, Hadoop...
Data Processing
buffer
Crail
Data Management
DiSNI
No data copies,
no context switches, no cache pollution,
very thin callstack
Runtime
Linux
Operating System
Fast Hardware
Flash
DRAM
Infiniband
JVM I/O bypass

---
The Crail Project: Diversity View
- Contains three types of components:
  - Crail Modules: implement higher-level I/O operations
  - Crail File System: backbone for any data movement
  - Crail storage backends: storage/network specific binding
- Crail's main features
  - Designed for high-performance networking and storage hardware
  - Designed explicitly for user-level storage and networking APIs
  - Designed to be completely pluggable (modules) and extendible (storage)

---
Crail Plugin Modules
Cores
Map
Crail
Reduce
Crail
Shuffle Module
Task
File
Directory
Sorted key range
Shuffle
- Spark specific plugin
- Maps key ranges to Crail dir’s
- Selects storage affinity in order of best performance
Broadcast
Spark specific plugin
Stores broadcast variables as Crail files
HDFS Adaptor
Generic plugin
Exports HDFS API

---
Evaluation – Terasort on OpenPOWER
Evaluation – Terasort
128 nodes OpenPOWER cluster
  1. 2 x IBM POWER8 10-core @ 2.9 GHz
  2. DRAM: 512GB DDR4
  3. 4 x 1.2 TB NVMe SSD
  4. 100GbE Mellanox ConnectX-4 EN (RoCE)
  5. Ubuntu 16.04 (kernel 4.4.0-31)
  6. Spark 2.0.2

---
Evaluation – Terasort
128 nodes OpenPOWER cluster
  1. 2 x IBM POWER8 10-core @ 2.9 GHz
  2. DRAM: 512GB DDR4
  3. 4 x 1.2 TB NVMe SSD
  4. 100GbE Mellanox ConnectX-4 EN (RoCE)
  5. Ubuntu 16.04 (kernel 4.4.0-31)
  6. Spark 2.0.2
6x
Performance gain: 6x
Most gain from reduce phase:
Crail shuffler much faster than Spark build-in
Dramatically reduced CPU involvement
Dramatically improved network usage
Map phase: all activity local
Still faster than vanilla Spark
12.8 TB data set, TeraSort
Runtime (secs)

---
Evaluation – TeraSort: Network IO
Evaluation – Network IO
- Vanilla Spark runs on 100GbE
- Spark/Crail runs on 100Gb RoCE/RDMA
- Vanilla Spark peaks at ~10Gb/s
- Spark/Crail shuffle delivers ~70Gb/s

---
Sorting Comparison
- Spark/Crail CPU efficiency is close to 2016 sorting benchmark winner: 3.13 vs. 4.4 GB/min/core
- 2016 winner runs native C code!

---
Crail is Open Source!
https://github.com/zrlio
www.crail.io

---
Related Work
Three classes of related work:
- New Data Processing Systems for High-Performance Network & Storage Hardware
  - FARM, RamCloud, HERD, etc
    Fast, but mostly academic, proprietary interfaces
- Updates/patches to existing Systems
  - Ohio Spark/Hadoop Distro
    Slow because no radical changes possible: fetrofitting RDMA/Flash integration into existing file/socket based I/O stacks
- Memory/Flash caches/stores
  - Example: Tacyon
    Slow because not designed for high-performance hardware

---
Conclusion
Today's open source analytics stacks:
- Existing analytics stacks designed for yesterday's commodity hardware
- Performance on high-end hardware inhibited by heavy-layered stack architecture
- Radical re-design of I/O (network & storage) for analytics by exploiting modern hardware
  - RDMA, NVMe & NVMe over fabrics
- Enable high-performance disaggregated storage for analytics
- Extend Spark operation to take advantage of Crail
- Crail is open source: www.crail.io
The Crail Approach:

---
The Crail Store
The Crail Store
directory
“/”
multifile
“tmp”
“shuffle”
file
Crail File System (Core)
DRAM
BlkDv
NVMef
GPU
BlkDev
High-performance RDMA cluster
Storage nodes
Flash blocks

---
Crail Storage Tiering
Traditional Vertical Tiering
Crail Horizontal Tiering
Tier fill order
Tier fill order
Node 1
Node 2
Node 3
Node 1
Node 2
Node 3
With horizontal tiering, higher-performing tiers are filled up across the cluster
prior to using lower performing tiers
DRAM
3DXP
Flash
DRAM
3DXP
Flash
DRAM
3DXP
Flash
DRAM
3DXP
Flash
DRAM
3DXP
Flash
DRAM
3DXP
Flash
Tier fill order
Tier fill order